What to Do When It is
Already Too Late ?
Crashdumps for Embedded Systems
Christoph Sterz christoph.sterz@kdab.com

---
Section slide
Embrace the Fail ❤️

---
Contents
- The Nature of a Crash and where to Intercept
- Coredumps, Signal Handlers and Daemons
- Google Breakpad & Sentry Native
- Get it all into Yocto
- On Collecting Crashdumps in production

---
Scope of “Crashes“ in this Talk
- Crashes mostly in C/C++
- On Embedded Linux
- Crashes induced from the inside and from the outside
- No Kernelpanics, Etc.
- SW-Devs’ Assumption #1: Hardware just Works

---
Crashes in Development And Production
- Dev Environment on Embedded Devices
  - All Symbs / (Remote) GDBs
  - Fullsize Dumps
  - EvalBoards
  - Small Testing Surface
- In Production
  - Slim Images
  - Slim Dumps / Reduced Bandwidth
  - (Often more limited) production hardware
  - Large Testing Surface

---
Programs crash from the inside out
libs / frameworks
& your code
c-runtime
process
systemd, systemv, appmanager, OS
hardware
v
v

---
Quick Setup: Enable Coredumps
Image : Jussi Kilpelainen

---
Prerequisits
- CONFIG_COREDUMP enabled in the Kernel
- Executable must be readable (Guess Why?)
- Process must have permissions to write the core
- You need enough space to store it
- You need enough Bandwidth to transfer it

---
Enable by setting limits

---
/proc/sys/kernel/core_pattern
Path containing %P %u %g %s %t %c %h
hostname
coresize
PID
uid
gid
signal
time of dump

---
CoreDumps: Did you know?
- You can madvise memorypages to be excluded from Coredump
  - Use madvise with MADV_DONTDUMP flag
- You can pipe coredumps to stdin of another process
  - Make your corePattern start with a | character, followed by the receiving process
  - SystemD coredumpctl does It |/usr/lib/systemd/systemd-coredump
- GDBs gcore can create a core of a running process

---
Poor-Man’s SlimDump: Backward-Cpp

---
By François-Xavier Bourlet, @bombela
The Pitch
Tired of seeing this ?

---
Then Try this :)

---
BackwardCpp
- This falls in the “Development”-situation category
- Include a header + 1 Line of initialization
- Symbols are necessary in build (-g), fat binaries
- Does Stack Unwinding in the signal handlers
- Requires the source code to print it
- Can be heavily customized
  → This is great for Development!

---
The Sanitizers can help you as well.

---
No Symbols? / Unwinding Fails?
Try “Desperate-Stack-Reading”

---
Signal Handlers can act
when its already too late
But they are limited
– use them with care!

---
Linux kill / OOMKiller
🔪
Program
Signalhandler
Signal proc mask
🎭
OS sends signal

---
Things not allowed in the SignalHandler
- Heap allocations are forbidden from this point on
- One is only permitted to execute “safe” operations
  - That is basically everything that does not allocate
  - Check man signal-safety for it
  - Code looks much like pure C-Code then
- Be hyper-careful of Crashes in Crash Handlers.
  You have been warned :)

---
Things which are (surprisingly)
allowed in the SignalHandler
- Start new processes (wow!)
- Obviously reading heap memory
- Again, everything that man signal-safety allows you to do
- Send signal to self

---
Cool Things possible in the Signal Handler
- Check out the KDABs QML StacktraceDumper.
  - Actually unsafe, because allocates
  - but worth the gamble, its too late anyways, right?
- Start new processes (wow!)

---
Watchdog-like processes can assist

---
It makes sense to have Watchdogs
out of the main execution Context
- There is not only Crashes, but also infinite loops
  - Idea: Reset the watchdog periodically, such that infinite loops are detected
- It can make a lot of sense to inject SIGSEGV & friends from the outside
- A stacktrace will still be produced and Analysis is possible

---
OOMkiller
- Most famous external source of an unwanted termination
- Stackdumps are of limited use in Analysis here
- Sends SIGKILL in rare cases also SIGTERM
  - Catch them and act accordingly (record the memory situation)

---
In Testing and Production:
Breakpad + Sentry on Yocto

---
General Architecture
SymbolServer
Email
SentryServer
Yocto
App
⚡
Crash
Hardware
Symbols

---
Google Breakpad
- Uses Minidumps
  - Originally envisioned by Microsoft
  - Similar to Slimcores, but way smaller (around 20KiB)
  - Can work with split symbols
  - Cross-platform
- Minidump comes with tools
  - Tore

---
Sentry Server

---
Getting it all Together for Yocto

---
Symbols are large…

---
End Of Talk!
I will answer all questions, AMA!