What to Do When It is
Already Too Late ?
Crashdumps for Embedded Systems
Christoph Sterz christoph.sterz@kdab.com

---
Section slide
❤️ Embrace the Fail

---
Content
- The nature of a crash and where to intercept
- Working with core dumps
- Signal handlers and watchdogs
- My serving suggestion:
  - Yocto, and…
  - Google Breakpad, and…
  - Sentry
- On collecting crashdumps in production

---
Scope of Crashes in this Talk
- Crashes mostly in C/C++
- On Embedded Linux
- Crashes induced from the inside and from the outside
- No Kernelpanics, etc.
- SW-Devs’ Assumption #1: Hardware just works

---
breakpad.bbclass contains this, always executed for a class inheriting breakpad
Crashes in Development And Production
Dev Environment on Embedded Devices
  - All Symbs / (Remote) GDBs
  - Fullsize dumps
  - EvalBoards
  - Small Testing Surface
- In Production
  - Slim Images
  - Slim Dumps / Reduced Bandwidth
  - (Often more limited) production hardware, no storage
  - Large Testing Surface

---
breakpad.bbclass contains this, always executed for a class inheriting breakpad
Crashes in Development And Production
Dev Environment on Embedded Devices
  - All Symbs / (Remote) GDBs
  - Fullsize dumps
  - EvalBoards
  - Small Testing Surface
- In Production
  - Slim Images
  - Slim Dumps / Reduced Bandwidth
  - (Often more limited) production hardware, no storage
  - Large Testing Surface
Boils down to
storage <vs.> no storage

---
Crashdumps and Symbols
App
App
App
App
App with
Symbols
App with
Symbols
- Symbols are needed:
  - To make addresses readable for humans
  - To reconstruct the contents of the Stack
  - To infer Line Numbers
- You will get symbols with -g
- Symbols are independent of optimization (-g, -O2)
- Symbols are huge 😅
Symbols
Symbols
stripping
stripping
App
App
App
App with
Symbols
Symbols
Symbols
unstripping
#3 foo(…)
#2 bar(…)
#1 baz(…)
#0 fail(...)
Symbols
Memory
Dump
Stacktrace
 (stack)
unwinding

---
Code is embedded
in many
execution
contexts.
libs / frameworks
& your code
c-runtime
process
systemd, systemv, appmanager, OS
hardware
v
v

---
4 Bytes of Core Memory : Arduino Module
Coredumps
Image : Jussi Kilpelainen
Image : Jussi Kilpelainen

---
What do Coredumps Look Like?
TODO

---
Prerequisites
- CONFIG_COREDUMP enabled in the Kernel
- Executable must be readable (guess why?)
- Process must have permissions to write the core
- You need enough space to store it
- You need enough Bandwidth to transfer it

---
Enable by setting limits

---
/proc/sys/kernel/core_pattern
Path containing %P %u %g %s %t %c %h
hostname
coresize
PID
uid
gid
signal
time of dump

---
CoreDumps: Did you know?
- You can madvise memorypages to be excluded from Coredump
  - Use madvise with MADV_DONTDUMP flag
- You can pipe coredumps to stdin of another process
  - Make your corePattern start with a | character, followed by the receiving process
  - Systemd coredumpctl does It |/usr/lib/systemd/systemd-coredump
- GDBs gcore can create a core of a running process

---
Development: have GDB on your target!
- At the Development Stage, just have a gdb on the target
- Find a way to store the coredump
- If you get a Crash producing a coredump, rejoin symbols:
  - Use the elfutils bin eu-unstrip <executable> <symbols>
  - Repeat for all relevant libraries you need for heap / stack
- Its a bit tedious, its worth it, if you need heap information
- If no heap is needed, there are better ways

---
You need it all for Cross-Platform CoreDumps 😬
- A cross-toolchain GDB on your Desktop
- The exact same executable that crashed (/w symbols)
- Symbols for all relevant libs when it crashed
- The core file
- Optionally /proc/kallsyms from the target
- Carefully feed SDK-Paths and Libs and see if you get a stack

---
GDB-Server: A Hybrid
App
symbols
Lib
symbols
executable
cross-gdb
gdbserver
host
target

---
Poor-Man’s SlimDump: Backward-Cpp

---
By François-Xavier Bourlet, @bombela
– The Pitch
Tired of seeing this ?

---
Then Try this :)

---
BackwardCpp
- This is in the Development-Situation category
- Include a header + 1 Line of initialization
- Symbols are necessary in build (-g), fat binaries
- Does stack unwinding in the signal handlers
- Requires the source code to print it
- Can be heavily customized
  → This is great for Development!

---
The Sanitizers can help you as well.

---
Crash output of an executable, instrumented with the gcc/clang address sanitizer

---
No Symbols?, Unwinding Fails?
You can still resort to:
»Desperate-Stack-Reading«

---
Printing raw stack memory, garnished with symbols
take everything with teaspoons of salt

---
Signal Handlers can act
when its already too late
But they are limited
– use them with care!

---
Linux kill / OOMKiller
🔪
Program
Invalid Memory Access
Signalhandler
Signal proc mask
🎭
OS sends signal

---
Things not allowed in the SignalHandler
- Heap allocations are forbidden from this point on
- One is only permitted to execute “safe” operations
  - That is basically everything that does not allocate
  - Check man signal-safety for it
  - Code looks much like pure C-Code then
- Be hyper-careful of Crashes in Crash Handlers.
  You have been warned :)

---
Things allowed in the SignalHandler
- Start new processes (wow!)
- Obviously reading heap memory
- Again, everything that man signal-safety allows you to do
- Send signal to self

---
Signalhandlers / Crashhandlers look much like plain C Code

---
🕶️ Cool Things possible in the Signal Handler
- Check out the KDABs QML stack trace dumper[1].
  - Actually unsafe, because allocates
  - but worth the gamble, its too late anyways, right?
- TODO More
  [1]https://github.com/KDAB/KDToolBox/tree/master/qt/qml/QmlStackTraceHelper

---
Watchdog-like processes can assist

---
It makes sense to have Watchdogs
out of the main execution Context
- There is not only Crashes, but also infinite loops
  - Idea: Reset the watchdog periodically, such that infinite loops are detected
- It can make a lot of sense to inject SIGSEGV & friends from the outside
- A stacktrace will still be produced and Analysis is possible

---
The OOM killer
- Most famous external source of an unwanted termination
- Stackdumps are of limited use in Analysis here
- Sends SIGKILL in rare cases also SIGTERM
  - Here, app dumps are a bit less interesting
  - Collect specificly the system-wide memory situation in this case

---
In Practice:
Google Breakpad + Sentry + Yocto

---
General Architecture
SymbolServer
Email
Yocto
Break-
pad
Dump
Extra
Info
App
Recipe
Breakpad
Handler
⚡
 handle&react
Crash
(changes)
App
Hardware
Symbols

---
Integrate Google Breakpad into Yocto
- Breakpad Recipes included in meta-oe/recipes-devtools
  - Creates all cross-tools needed
  - Creates the header-only library needed for the custom Signal Handler
  - Provides a yocto bbclass to be added to your app recipe
    - This then splits out symbols before app-binary is stripped by yocto
- Extras can be added in your individual app recipe
Symbols

---
breakpad.bbclass contains this, always executed for a class inheriting breakpad
myapp.bb: I extend the breakpad step to have 2 executables and do the upload on every build
… now every yoctobuild uploads the symbols !

---
For the other libs, I use the yocto-built SDK, it contains split debug symbols in .debug folders
Example for file libQt5Core.so : It is important, that debug info is present
… from there it is uploaded like all symbs with sentry-cli

---
More Infos on Googles Breakpad
- Uses Minidumps
  - Originally envisioned by Microsoft
  - Similar to slim cores, but way smaller (around 20KiB)
  - Cross-platform (unix cores don’t work on Windows, settled on minidump)
  - Splitting command: dump_symbs executable > /path/to/destination.symbs
- Minidump comes with some useful tools
  - minidump_stackwalk: Re-Combine Minidump+App+Symbols → get a stack
  - minidump-2-core: Converts dump to gdb-readable format
  - and more…

---
Integrate Breakpad in your Code
- Breakpads library and headers are included in the new SDK
  when using it in any of your recipes
- Only 2 extra lines in main() are necessary to register
- Of course you can do more in your custom Handler
libbreakpad_client.a
Breakpad
Handler
App

---
Register the handler in your main(), pass any variables to be used
Register Breakpad
Handler
Include Breakpad Header,
Handle crashes and write extra information
Write Extra Information

---
Sending the Information
- Let a daemon check the crash folder for crashes
  - Not known if device has connectivity
  - Daemon checks periodically if a minidump is available
  - If allowed in the User-settings, Info is uploaded to the sentry server
- For now, no logs are uploaded, maybe in the future…
Daemon
Break-
pad
Dump
Extra
Info
Breakpad
Handler
Hardware
⚡
App
Crash

---
Snip from the Crashdaemon,
A file watcher looks for crash data and uploads it, when possible
Extra tag info is garnished for sentry

---
The Result
//Categorized

---
The Result(II)
//Extra Information
//Breakpad Information
//Symbols available
//Symbols not available

---
Mail 💌

---
More about sentry
- FOSS Dump Collector
- Sorts Crashes by Stack, configurable
- Supports many DumpFormats
- Suppports external Symbol Servers
- ~30€/mo or self hosted

---
GDPR?
<Im not a lawyer>, but… ⚖️

---
On uploading crash(=user)data
- We run it for development / staging / testing only
- If Production is involed, make it opt-In for users
- Practically, stack information might contain all information
- If dumps are anonymized and users know for what purpose the data is collected, one should be fine
  … </but Im not a lawyer>

---
#1
Overall there is still much to do,
when its already too late
I showed you classic ways in therory
and one way I like in practice
Invest in learning from your crashes—it is worth it.
#2
#3

---
End Of Talk!
I will answer all questions, AMA!